ARCHITETTURA INTERNA, SET ISTRUZIONI E PIEDINATURA DELLO Z80

### Main instructions

|  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | nop | ld bc,** | ld (bc),a | inc bc | inc b | dec b | ld b,* | rlca | ex af,af' | add hl,bc | ld a,(bc) | dec bc | inc c | dec c | ld c,* | rrca |
| 1 | djnz * | ld de,** | ld (de),a | inc de | inc d | dec d | ld d,* | rla | jr * | add hl,de | ld a,(de) | dec de | inc e | dec e | ld e,* | rra |
| 2 | jr nz,* | ld hl,** | ld (**),hl | inc hl | inc h | dec h | ld h,* | daa | jr z,* | add hl,hl | ld hl,(**) | dec hl | inc l | dec l | ld l,* | cpl |
| 3 | jr nc,* | ld sp,** | ld (**),a | inc sp | inc (hl) | dec (hl) | ld (hl),* | scf | jr c,* | add hl,sp | ld a,(**) | dec sp | inc a | dec a | ld a,* | ccf |
| 4 | ld b,b | ld b,c | ld b,d | ld b,e | ld b,h | ld b,l | ld b,(hl) | ld b,a | ld c,b | ld c,c | ld c,d | ld c,e | ld c,h | ld c,l | ld c,(hl) | ld c,a |
| 5 | ld d,b | ld d,c | ld d,d | ld d,e | ld d,h | ld d,l | ld d,(hl) | ld d,a | ld e,b | ld e,c | ld e,d | ld e,e | ld e,h | ld e,l | ld e,(hl) | ld e,a |
| 6 | ld h,b | ld h,c | ld h,d | ld h,e | ld h,h | ld h,l | ld h,(hl) | ld h,a | ld l,b | ld l,c | ld l,d | ld l,e | ld l,h | ld l,l | ld l,(hl) | ld l,a |
| 7 | ld (hl),b | ld (hl),c | ld (hl),d | ld (hl),e | ld (hl),h | ld (hl),l | halt | ld (hl),a | ld a,b | ld a,c | ld a,d | ld a,e | ld a,h | ld a,l | ld a,(hl) | ld a,a |
| 8 | add a,b | add a,c | add a,d | add a,e | add a,h | add a,l | add a,(hl) | add a,a | adc a,b | adc a,c | adc a,d | adc a,e | adc a,h | adc a,l | adc a,(hl) | adc a,a |
| 9 | sub b | sub c | sub d | sub e | sub h | sub l | sub (hl) | sub a | sbc a,b | sbc a,c | sbc a,d | sbc a,e | sbc a,h | sbc a,l | sbc a,(hl) | sbc a,a |
| A | and b | and c | and d | and e | and h | and l | and (hl) | and a | xor b | xor c | xor d | xor e | xor h | xor l | xor (hl) | xor a |
| B | or b | or c | or d | or e | or h | or l | or (hl) | or a | cp b | cp c | cp d | cp e | cp h | cp l | cp (hl) | cp a |
| C | ret nz | pop bc | jp nz,** | jp ** | call nz,** | push bc | add a,* | rst 00h | ret z | ret | jp z,** | BITS | call z,** | call ** | adc a,* | rst 08h |
| D | ret nc | pop de | jp nc,** | out (*),a | call nc,** | push de | sub * | rst 10h | ret c | exx | jp c,** | in a,(*) | call c,** | IX | sbc a,* | rst 18h |
| E | ret po | pop hl | jp po,** | ex (sp),hl | call po,** | push hl | and * | rst 20h | ret pe | jp (hl) | jp pe,** | ex de,hl | call pe,** | EXTD | xor * | rst 28h |
| F | ret p | pop af | jp p,** | di | call p,** | push af | or * | rst 30h | ret m | ld sp,hl | jp m,** | ei | call m,** | IY | cp * | rst 38h |

### Extended instructions (ED)

|  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 4 | in b,(c) | out (c),b | sbc hl,bc | ld (**),bc | neg | retn | im 0 | ld i,a | in c,(c) | out (c),c | adc hl,bc | ld bc,(**) | neg | reti | im 0/1 | ld r,a |
| 5 | in d,(c) | out (c),d | sbc hl,de | ld (**),de | neg | retn | im 1 | ld a,i | in e,(c) | out (c),e | adc hl,de | ld de,(**) | neg | retn | im 2 | ld a,r |
| 6 | in h,(c) | out (c),h | sbc hl,hl | ld (**),hl | neg | retn | im 0 | rrd | in l,(c) | out (c),l | adc hl,hl | ld hl,(**) | neg | retn | im 0/1 | rld |
| 7 | in (c) | out (c),0 | sbc hl,sp | ld (**),sp | neg | retn | im 1 |  | in a,(c) | out (c),a | adc hl,sp | ld sp,(**) | neg | retn | im 2 |  |
| A | ldi | cpi | ini | outi |  |  |  |  | ldd | cpd | ind | outd |  |  |  |  |
| B | ldir | cpir | inir | otir |  |  |  |  | lddr | cpdr | indr | otdr |  |  |  |  |

### Bit instructions (CB)

|  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | rlc b | rlc c | rlc d | rlc e | rlc h | rlc l | rlc (hl) | rlc a | rrc b | rrc c | rrc d | rrc e | rrc h | rrc l | rrc (hl) | rrc a |
| 1 | rl b | rl c | rl d | rl e | rl h | rl l | rl (hl) | rl a | rr b | rr c | rr d | rr e | rr h | rr l | rr (hl) | rr a |
| 2 | sla b | sla c | sla d | sla e | sla h | sla l | sla (hl) | sla a | sra b | sra c | sra d | sra e | sra h | sra l | sra (hl) | sra a |
| 3 | sll b | sll c | sll d | sll e | sll h | sll l | sll (hl) | sll a | srl b | srl c | srl d | srl e | srl h | srl l | srl (hl) | srl a |
| 4 | bit 0,b | bit 0,c | bit 0,d | bit 0,e | bit 0,h | bit 0,l | bit 0,(hl) | bit 0,a | bit 1,b | bit 1,c | bit 1,d | bit 1,e | bit 1,h | bit 1,l | bit 1,(hl) | bit 1,a |
| 5 | bit 2,b | bit 2,c | bit 2,d | bit 2,e | bit 2,h | bit 2,l | bit 2,(hl) | bit 2,a | bit 3,b | bit 3,c | bit 3,d | bit 3,e | bit 3,h | bit 3,l | bit 3,(hl) | bit 3,a |
| 6 | bit 4,b | bit 4,c | bit 4,d | bit 4,e | bit 4,h | bit 4,l | bit 4,(hl) | bit 4,a | bit 5,b | bit 5,c | bit 5,d | bit 5,e | bit 5,h | bit 5,l | bit 5,(hl) | bit 5,a |
| 7 | bit 6,b | bit 6,c | bit 6,d | bit 6,e | bit 6,h | bit 6,l | bit 6,(hl) | bit 6,a | bit 7,b | bit 7,c | bit 7,d | bit 7,e | bit 7,h | bit 7,l | bit 7,(hl) | bit 7,a |
| 8 | res 0,b | res 0,c | res 0,d | res 0,e | res 0,h | res 0,l | res 0,(hl) | res 0,a | res 1,b | res 1,c | res 1,d | res 1,e | res 1,h | res 1,l | res 1,(hl) | res 1,a |
| 9 | res 2,b | res 2,c | res 2,d | res 2,e | res 2,h | res 2,l | res 2,(hl) | res 2,a | res 3,b | res 3,c | res 3,d | res 3,e | res 3,h | res 3,l | res 3,(hl) | res 3,a |
| A | res 4,b | res 4,c | res 4,d | res 4,e | res 4,h | res 4,l | res 4,(hl) | res 4,a | res 5,b | res 5,c | res 5,d | res 5,e | res 5,h | res 5,l | res 5,(hl) | res 5,a |
| B | res 6,b | res 6,c | res 6,d | res 6,e | res 6,h | res 6,l | res 6,(hl) | res 6,a | res 7,b | res 7,c | res 7,d | res 7,e | res 7,h | res 7,l | res 7,(hl) | res 7,a |
| C | set 0,b | set 0,c | set 0,d | set 0,e | set 0,h | set 0,l | set 0,(hl) | set 0,a | set 1,b | set 1,c | set 1,d | set 1,e | set 1,h | set 1,l | set 1,(hl) | set 1,a |
| D | set 2,b | set 2,c | set 2,d | set 2,e | set 2,h | set 2,l | set 2,(hl) | set 2,a | set 3,b | set 3,c | set 3,d | set 3,e | set 3,h | set 3,l | set 3,(hl) | set 3,a |
| E | set 4,b | set 4,c | set 4,d | set 4,e | set 4,h | set 4,l | set 4,(hl) | set 4,a | set 5,b | set 5,c | set 5,d | set 5,e | set 5,h | set 5,l | set 5,(hl) | set 5,a |
| F | set 6,b | set 6,c | set 6,d | set 6,e | set 6,h | set 6,l | set 6,(hl) | set 6,a | set 7,b | set 7,c | set 7,d | set 7,e | set 7,h | set 7,l | set 7,(hl) | set 7,a |

PIEDINATURA